## Slide 1
EV3 Classroom: Basic Turning
BEGINNER PROGRAMMING LESSON

## Slide 2: Lesson Objectives
Learn to turn the robot a desired number of degrees
Learn the differences between Spin and Pivot Turns
Learn how to program two different type of turns
Learn to write pseudocode

## Slide 3: PIVOT Vs. SPIN Turns
180 Degree Pivot Turn
180 Degree Spin Turn
Notice where the robot ends in both pictures after a 180 degree turn.
In the Spin Turn, the robot moves a lot less and that makes Spin Turns are great for tight positions. Spin turns tend to be a bit faster but also a little less accurate.
So when you need to make turns, you should decide which turn is best for you!
B
C
Start Position
End Position
Motors
B and C Move
B
C
Motor
B Moves
Start Position
End Position
B
C
B
C

## Slide 4: How to Make Pivot and Spin turns
Steering Value |  |  | 
50 | -50 | 100 | -100
Pivot Turn Right | Pivot Turn Left | Spin Turn Right | Spin Turn Left
Change Steering value here
B
C
B
C
B
C
B
C
Move Steering Block

## Slide 5: Move steering
Found in the movement tab in the palette
The first input (by default straight) determines the steering value. It ranges -100 to 100.
The second input determines the distance to travel and its unit (rotations, degrees, or seconds). We will be using degrees.
The 3rd input determines the speed of the robot (range of -100 to 100).
Tip: use the Control block Stop ( ) to end the program at the end of your project

## Slide 6: MAKING A Pivot turn for 90 DEGREES
Program your robot to turn 90 degrees
Does the robot actually turn 90 degrees if you just pick 90 degrees for distance?
B
C
B
C
?
Ans. NO! Solution on next page

## Slide 7: how do you make the robot turn 90 degrees?
Ans. Try using the port view to measure the turn and then input the correct number of degrees. For the EV3 Educator robot, it is 360 degrees.

## Slide 8: TEACHER INSTRUCTIONS
Split up class into groups as needed
Give each team a copy of the Turning Challenge Worksheet
Challenge Details are on Slide 9
Discussion Page Slide 10
Challenge Solution on Slide 11

## Slide 9: TURNING CHALLENGES
Challenge 2
Your robot baseball player must run to second base, turn around and come back to first.
Go straight. Turn 180 degrees and return to the same spot.
B
C
Challenge 1
Your robot is a baseball player who has to run to all the bases and go back to home plate.
Can you program your robot to move forward and then turn left?
Use a square box or tape
Start and End position
First Base
B
C
Second Base

## Slide 10: CLASS Discussion GUIDE
Did you try PIVOT and SPIN turns? What did you discover?
  Pivot turns were fine for Challenge 1, but for Challenge 2, if we used Pivot turns, we were farther away from the base.
What situations would one work better than the other?
  Spin turns are better for tight turns (places where there is not enough space) and you stay closer to your original position.
What is PSEUDOCODE? Why do you think programmers find it useful? (pseudocode is from the worksheet)
  Pseudocode allows programmers to write out their code in plain English before you code in a programming language. It lets you plan and think before you sit down to code. It lets you share your ideas with others you are working with in a common language.

## Slide 11: CHALLENGE SOLUTIONS
Challenge 2
You probably used a spin turn because it is better for tighter turns and gets you closer to the starting point!
Challenge 1
You probably used a combination of move steering to go straight and do pivot turns to go around the box.
B
C
Start and End position
First Base
B
C
Second Base

## Slide 12: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan
More lessons are available at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.