## Slide 1: INTERMEDIATE PROGRAMMING LESSON
Different Ways of moving:
Synchronization, Regulated power, Ramp UP & down

## Slide 2: Objectives
1) Learn about different blocks for moving the robot and when to use which block
2) Learn about power regulation, motor synchronization, and ramp up/down

## Slide 3: Different Ways To Move
How are these different from each other in terms of the following?
  Power Regulation
  Motor Synchronization
  Ramp up/ramp down
1
2
3
4

## Slide 4: Regulated Power
Regulated power tries to move the robot at a fixed target speed
When the robot has trouble moving because it is heavy, it is moving uphill, its battery is dead, or it is blocked, power regulation gives more power to the motor to reach its target speed
This is good for ensuring that the robot is moving at a predictable speed

## Slide 5: Synchronized Motors
Synchronized motors makes sure that both motors turn the same amount (or at some fixed ratio)
If one wheel gets stuck, it prevents the other wheel from spinning
If you have the motors turning the same amount, it helps ensure that the robot moves straight when one wheel is slowed by friction or anything else
When you have synchronized motors with a ratio, it makes the robot make predictable and smooth turns
Videos on next slide

## Slide 6: Synchronized vs. Unsynchronized
Synchronized motors
One motor getting stuck causes other motor to stop
Unsynchronized motors
Second motor continues when first gets stuck
Click to Watch Videos

## Slide 7: Ramp Up / Ramp Down
Ramp up makes the robot speed up gradually at the beginning of a move
Ramp down makes the robot brake gradually at the end
Without ramp up/ramp down you might see the robot jerk at the beginning or end
  The robot will still adjust its motors after a brake to reach that target rotation sensor value but this may still be less accurate

## Slide 8: Different Ways To Move
 |  |  | Regulated Power | Synchronized Motors | Ramp Up / Ramp Down
 |  |  | ✔ | ✔ | ✔
 |  |  | ✔ | ✔ | ✔
 |  |  | ✔ | ✗ | ✗
 |  |  | ✗ | ✗ | ✗
1
2
3
4

## Slide 9: Moving Degrees vs. Seconds
Move Degrees/Rotations
Block does not complete until the target degree rotation is reached
So what if the robot gets stuck somewhere on the mat?
  Program stalls and never goes to next block
  You will have to save the robot and take a touch penalty
Move Seconds
  Less accurate for robot movement
    Distance traveled depends on speed, battery level, weight of robot
  You have to remember this when deciding if move secs should be used.
  However, can help avoid stalls
    E.g. Can be useful if your attachment arm gets stuck
Videos on next slide

## Slide 10: Moving Degrees vs. Seconds
Stalled Robot
Robot gets stuck. Finishes only when released.
Unstalled Robot
Robot gets stuck but still finishes (you can hear the sound)
Click to Watch Videos

## Slide 11: Discussion Guide
 |  |  | Regulated Power | Synchronized Motors | Ramp Up / Ramp Down
1
2
3
4
Fill in the chart below:

## Slide 12: Credits
This tutorial was created by Sanjay Seshan and Arvind Seshan from Droids Robotics.
More lessons are available at www.ev3lessons.com
Author’s Email: team@droidsrobotics.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.